## Slide 1: Chapter 7 Fire Characteristics: Gaseous Combustibles

## Slide 2: Objectives
Describe the categorization of flames.
Characterize laminar and turbulent flames.
Define deflagration and detonation, and explain the difference between the two.
Discuss flammability limits and burning velocity, as well as their relationship to fire hazard.

## Slide 3: Objectives
Understand the difference between piloted ignition and autoignition.
Explain the potential hazard from a gas leak.
Explain the importance of chain branching in combustion chemistry.

## Slide 4: Gaseous Fuels
Oxidation of gaseous fuels generates a lot of heat.
Courtesy of the US Navy.

## Slide 5: Categorization of Flames
Categories of flame:
  Premixed/diffusion flames
  Laminar/turbulent flames
  Stationary/propagating flames
  Subsonic/supersonic flames
Most fires are subsonic, turbulent diffusion flames when particularly hazardous.

## Slide 6: Premixed Versus Diffusion Flames
Premixed flame example: residential gas leak and after a few minutes a person lights a match.
  Stoichiometric mixture according to: CH4 + 2O2 → 2H2O
  Burning velocity
  Percentage/ratio of oxygen and gaseous material affects flame propagation and peak temperature.

## Slide 7: Premixed Versus Diffusion Flames
Premixed flames can be stabilized to burn in a stationary position for measurement.

## Slide 8: Premixed Versus Diffusion Flames
Diffusion flame: fuel and oxidizer gases initially exist as separate volumes.
  Combustion occurs when an ignition source is placed near the interface of fuel and oxidizer.
  Diffusion flame temperatures are lower than premixed flames.

## Slide 9: Premixed Versus Diffusion Flames
Fires are predominantly diffusion flames, but stationary diffusion flames can be developed.

## Slide 10: Laminar Versus Turbulent Flames
© irin-k/ShutterStock, Inc.
© Tigergallery/ShutterStock, Inc.

## Slide 11: Laminar Versus Turbulent Flames: Laminar Flames
Smooth flow streamlines and negligible velocity component fluctuations
  Straight or gentle curving line
  Low Reynolds number value
  Diffusion flame shorter than 0.1 m (4 in.)
  Lower rates of combustion and convective heat loss

## Slide 12: Laminar Versus Turbulent Flames: Turbulent Flames
Significant fluctuations in velocity and temperature profiles
  Erratic particle paths
  High Reynolds number values
  Diffusion flame taller than 0.3 m (1 ft)
  Higher rates of combustion and convective heat loss

## Slide 13: Ignition of Gases
First step: generation of a species highly reactive enough to destabilize a fuel molecule
  Piloted ignition
  Auto-ignition

## Slide 14: Ignition of Gases
Ignition depends on:
  Energy of the spark
  Gaseous fuel
  Equivalence ratio of the fuel–air mixture
A near-stoichiometric mixture demonstrates the greatest sensitivity to ignition.

## Slide 15: Minimum Spark Ignition Energies
Fuel–oxygen mixtures ignite with weak sparks more easily than fuel–air mixtures.
  Saturated hydrocarbons all ignite similarly in air.
  Progressive unsaturation in a hydrocarbon molecule favors much easier ignition.

## Slide 16: Ignition Energy
The minimum ignition energy needed to ignite most fuel vapor–air mixtures is approximately inversely proportional to the square of the absolute pressure.
Gas mixtures can be ignited with an existing flame, introducing free radicals.

## Slide 17: Gas/Vapor–Air Mixtures
Can be ignited via contact with a surface hot enough to raise the mixture’s temperature
  Relative autoignition temperatures can be obtained for certain gases.

## Slide 18: Gas/Vapor–Air Mixtures
    Carbon disulfide is easier to ignite via thermal ignition than hydrogen.
    Hydrogen and carbon disulfide require similar ignition energies.
    Increases in molecular weight of saturated hydrocarbons requires a lower thermal ignition temperature.
    Acetylene is easier to ignite than ethane.

## Slide 19: Flammability Limits
Mixtures too rich or too lean are difficult to ignite and slower to burn.
  Nitrogen in a methane–air mixture absorbs some heat, lowers the temperature, and causes slower flame reactions.
  More nitrogen would cause the mixture to be nonflammable.
  Lean flammability limit (lean limit)
  Upper flammability limit (rich limit)

## Slide 20: Flammability Limits
Dilution of a methane–air mixture with nitrogen

## Slide 21: Flammability Limits
Wider at higher temperatures
Independent of pressure at ordinary and high pressures (> 50 kPa)
Approach each other at low pressures
  No propane–air mixture is flammable at < 4 kPa.

## Slide 22: Flammability Limits
Hydrogen, carbon disulfide, acetylene, and fuel vapors mixed with oxygen have wide flammability limits.

## Slide 23: Burning Velocity
Burning velocity: The speed with which a flame moves through unburned gas
Burning velocity is approximately proportional to (q″ × κ)1/2, where:
  q″ = mean rate of heat generation in the flame
  κ = thermal conductivity of gas mixture

## Slide 24: Burning Velocity
It is difficult to make absolute measurements of true burning velocities.
Most hydrocarbons have a similar magnitude of their burning velocity.

## Slide 25: Burning Velocity
A flame could move faster than its measured burning velocity if:
  Laboratory apparatus surfaces slow the flame movement.
  Flame raises the temperature of the gas enough to cause motion and carry the flame toward unburned gas.
  Flame is a turbulent premixed flame.

## Slide 26: Explosions, Deflagrations, and Detonations
Explosion: The rapid release of energy and increase in pressure when a premixed flame propagates in a confined space
Deflagration: Subsonic combustion
Detonation: Supersonic combustion

## Slide 27: Explosions, Deflagrations, and Detonations
Deflagration
  Propagates at subsonic velocity
  Burning velocity depends on chemically controlled rate of heat release in the flame.
  Diffusion flames are typically deflagrations.

## Slide 28: Explosions, Deflagrations, and Detonations
Detonation
  Propagates at supersonic velocity
  Velocity is calculated with the heat of combustion and the physical properties of the mixture.
Damage from a detonation is generally due to the generated high pressure.

## Slide 29: Hydrogen Oxidation
Chain reaction
Most critical step:
  H + O2 → OH + O
  Chain branching reaction
Next step:
  OH + H2 → H2O + H
  Chain propagation reaction

## Slide 30: Hydrogen Oxidation
Next step:
  O + H2 → OH + H
This branching sequence of reactions leads to an H2–O2 explosion.

## Slide 31: Hydrogen Oxidation
Sequence continues until one or both reactants is consumed.
  Chain termination reactions
  H + O → OH and H + OH → H2O
The hydrogen oxidation reaction is unique in its small number of chemical species and reactions.

## Slide 32: Premixed Methane–Oxygen Flame Chemistry
Methane is the simplest hydrocarbon fuel but still involves 53 chemical species and 325 reactions.
Methane–oxygen reaction involves chain initiation, propagation, branching, and termination steps.

## Slide 33: Premixed Methane–Oxygen Flame Chemistry

## Slide 34: Combustion of Larger Hydrocarbon Fuels
Fuels with a greater number of carbon atoms involve greater numbers of chemical species and reactions for the flame mechanism.

## Slide 35: Hydrogen (H2)
Among the most dangerous gases (fire-wise)
  Odorless
  Almost invisible flame

## Slide 36: Hydrogen (H2)
Wide flammability limits
Easily ignited when mixed with air
Higher burning velocity than any other combustible

## Slide 37: Hydrogen (H2)
Flammable levels of hydrogen are generated in well-known situations.
Hydrogen is light.
Can rise to the upper area of a compartment

## Slide 38: Acetylene (C2H2)
Extremely reactive and flammable
Must be stored in cylinders filled with porous mass
Can be effectively stored as liquid, but flows out as gas
Wide flammability limits

## Slide 39: Acetylene (C2H2)
Fusible plug that opens at 212 °F is required in all acetylene tanks in North America.
Acetylene–air flames propagate rapidly.
Copper and copper alloys are not used in storing or delivering acetylene.

## Slide 40: Methane (CH4)
Odorless gas
Lighter than air
Main constituent of natural gas
Flammability similar to other saturated hydrocarbon gases

## Slide 41: Ethylene (C2H4)
Industrial gas
Faint, sweet odor
Ethylene–air mixtures, compared to saturated hydrocarbon-air mixtures:
  Wider flammability limits
  Easier to ignite
  More rapid flame propagation
  Can detonate
More luminous flames

## Slide 42: Ammonia (NH3)
Commercial refrigerant and fertilizer
Sharp, pungent odor
Ammonia–air mixtures, compared to hydrocarbon-air mixtures:
  Difficult to ignite
  Burn more slowly
© TPG/TOPHO/AP Images

## Slide 43: Summary
The molecules that combust in a flaming fire are nearly always in the gas phase.
Flames can be characterized as premixed or diffusion, laminar or turbulent, and stationary or propagating. A deflagration is a subsonic flame; a detonation is a supersonic flame.

## Slide 44: Summary
Mixtures of fuel and air are flammable if the fuel concentration is greater than the lean flammability limit and less than the rich flammability limit.
A premixed flame has a higher burning velocity than a diffusion flame of the same fuel. The burning rate of the former is determined by the flame chemistry; the burning rate of the latter is determined by the diffusion of fuel and air into each other.

## Slide 45: Summary
Piloted ignition is the ignition of a flammable mixture by a source that provides the high temperature and/or source of the free radicals needed to initiate the flame chemistry. Autoignition occurs when the temperature of the fuel–air mixture is high enough for the collision energy of the molecules to break the molecules’ bonds.

## Slide 46: Summary
Reactions for the combustion of fuel molecules include chain initiation steps, chain propagating steps, chain branching steps, and chain termination steps.

## Slide 47: Summary
The initiation steps create the free radicals that propagate the flame; the termination steps remove the free radicals, converting them into stable species. The chain branching steps multiply the number of active species in the flame, thus determining the number of simultaneous chain propagating steps. The key chain branching reaction step is H + O2 → OH + O.

## Slide 48: Summary
A leak of flammable gas can pose a serious fire hazard. Near the leak, the atmosphere is fuel rich. Far away from the leak, the atmosphere is fuel lean. If an ignition source is active in the region where the mixture is within the flammable limits, an explosion is possible.