## Slide 1: Chapter 13 Fire Fighting Chemicals

## Slide 2: Objectives
Distinguish among fire extinguishment, fire control, and fire inerting.
List the four classes of fire, as used in the United States.
Describe the different ways in which water suppresses a fire, depending on its method of delivery and the geometry of the fire, and list the types of fires on which water should not be applied.

## Slide 3: Objectives
Describe the roles of suppression-enhancing additives to water.
List the types of nonaqueous fire suppressants.

## Slide 4: Objectives
Understand why the use of halon for fire extinguishment has been curtailed.
Explain how powdered agents are effective for fire extinguishment.

## Slide 5: Introduction
Change in fire suppression chemistry
  Manufacture and use of fully halogenated fire suppressants curtailed
  New approaches developed

## Slide 6: Definitions
Flame or fire extinguishment
Fire control
Flame or fire suppression
Fire inerting

## Slide 7: Organization of Applied Chemicals
Types of fire on which they are effective:
  Class A
  Class B
  Class C
  Class D

## Slide 8: Organization of Applied Chemicals
Phase of the chemical
Mechanism of action:
  Interference with flame propagation
  Thermal interaction
  Dilution of fuel vapors and/or oxygen
  Separation of fuel and flames

## Slide 9: Organization of Applied Chemicals
Mode of application
  Streaming
  Total flooding
Application system

## Slide 10: Water
Oldest fire suppressant
Automatic sprinkler systems
  Actuation under most effective conditions
  Residential sprinklers
Response time index (RTI) given in units of:
  m1/2s1/2 (ft1/2s1/2)

## Slide 11: Water
Plunge test
Heat transfer from hot air to the sprinkler is approximately proportional to the square root of the flow velocity.

## Slide 12: Water
Equation 13-1: RTI = (Mt ct/hc A)v1/2
  Mt is the mass of the trigger.
  ct is the heat capacity of the trigger (J/g K).
  hc is the convective heat transfer coefficient from the air to the trigger (J/m2 Ks).
  A is the area of the trigger exposed to the hot air flow (m2).
  v is the air velocity (m/s).

## Slide 13: Water
Final units of the RTI are square root of length × square root of time.
Desirable features of using water:
  Readily available
  Low cost
  Nonflammable
  High heat of vaporization

## Slide 14: Water
Desirable features of using water (cont’d):
  Gasifies readily
  Expands upon vaporization
  Readily transportable at normal ambient temperature
  Nontoxic
  Limited property damage

## Slide 15: Water
Class considerations:
  Less desirable for Class B
  Used with care in Class C
  Should be avoided in Class D
Three effects of water to slow rate of combustion:
  Water substantially cools contacted fuel area.
  Hot surface vaporizes some of the water.
  Absorbs enthalpy

## Slide 16: Water
Size distribution of water droplets from a sprinkler:
  Too small
  Too large
© Ocean/Corbis.

## Slide 17: Water
Mean droplet diameter increases with the radial distance from the sprinkler axis.

## Slide 18: Water
Three variables for mean diameter of water droplets:
  Orifice diameter, D
  Pressure drop, ∆P
  Surface tension, σ
Equation 13-2: dd = c(σD2/ΔP)1/3
  c is a constant determined experimentally.

## Slide 19: Water
Surface tension of water
  Wetting agent
Delivery rate required to control a fire
  Water depth accumulated per unit time (mm/min or in./min)

## Slide 20: Water
Water mist
Fine water mist extinguishes a fire by one of four mechanisms:
  Removes heat
  Evaporates and generates steam
  Blocks radiative heat transfer
  Cools the fuel surface

## Slide 21: Enhanced Water
Water additives:
  Alter droplet size
  Improve ability to penetrate porous materials
  Increase efficiency for heat absorption
Adding chemicals (inorganic salts)

## Slide 22: Enhanced Water
Miscible organic compound
  Residual liquid could become flammable.
Fire hose or sprinkler system flow is determined by:
  Water pressure from the source
  Inner diameter of the hose or piping
  Resistance to flow of the moving water at the inner surface

## Slide 23: Enhanced Water
Friction-reducing additives
Thickening additives
Problems with thickening water:
  Poorer penetration of fuel masses
  Greater friction loss in hoses
  Inability to produce fine sprays
  Slippery floors
  Clean-up
Wildland fires

## Slide 24: Aqueous Foams
Common characteristics
Class B foams separate fuel from air
  Generally for large flammable liquid fires
Flammable organic fluids with densities lower than water
  Gasoline
  Oil or fat
  Deep pools of alcohols

## Slide 25: Aqueous Foams
Fireground conditions that negate benefits of aqueous foam:
  High winds
  Heat from the fire
  Chemical action of certain vapors
  Proportionally mixed with flowing water

## Slide 26: Aqueous Foams
Aqueous film-forming foam
  Film spreads over the surface of the fuel if the surface tension of the combustible liquid is greater than the surface tension of the AFFF solution by an amount in excess of the interfacial tension between the two liquids.
  Can penetrate a porous fuel mass
  Alcohol-resistant foaming agents

## Slide 27: Aqueous Foams
Protein foams
  Metal salt added
  Organic solvent added
  Higher surface tension than the values for AFFFs
  Biodegradable
Fluoroprotein foam
  Added surfactant
  Compatible with dry chemical fire suppressants

## Slide 28: Aqueous Foams
Medium- and high-expansion foam
  Control or extinguish fires
  More likely to stay on vertical surfaces
  Delicate/easily blown by wind
  Must be applied quickly and efficiently

## Slide 29: Aqueous Foams
Medium- and high-expansion foam (cont’d)
  Well suited for flooding confined spaces
Courtesy of USACE Photo.

## Slide 30: Nonaqueous Agents
Circumstances for alternative means of fire extinguishment:
  Cluttered, enclosed spaces
  Irreplaceable objects susceptible to water damage
  Service interruption
  Water storage and dispersion systems not practical
  Materials incompatible with water:
    Metals
    Inorganic chemicals
  Groundwater pollution
  Electric shock hazard

## Slide 31: Nonaqueous Agents
Nonaqueous fire suppressants:
  Inert gases
  Halogenated organic compounds
  Powdered inorganic salts

## Slide 32: Nonaqueous Agents

## Slide 33: Inert Gases
Clean agent
  More efficient inert gases
  Less efficient inert gases
Limitations of use:
  Enclosure not airtight
  Impractical to flood large compartment
  Supply exhaustion
  Cannot be projected very far

## Slide 34: Inert Gases
Cup burner
  Generally filled with n-heptane (C7H16)

## Slide 35: Inert Gases

## Slide 36: Inert Gases
Four groups of inert gases:
  Noble gases
  Nitrogen
  Carbon dioxide
  Fully fluorinated organic molecules

## Slide 37: Noble Gases
Noble gases
  Identical, very low molar heat capacities
  Helium, neon, argon, krypton
  40 volume percent added to the air
  Concern of asphyxiation
  Mix inert gases with CO2

## Slide 38: Nitrogen
Nitrogen
  One-third volume fraction addition to the air
  Compressed gas
  Cryogenic liquid
  Lightweight semipermeable membranes
  Reduces oxygen level to untenable point
  Certain metals react exothermically.

## Slide 39: Carbon Dioxide
Carbon dioxide is the most commonly used inert gas
More effective than nitrogen on a volume basis
  However, a given volume of carbon dioxide is 1.57 times as heavy as nitrogen, so the two gases have nearly equal effectiveness of a mass basis.

## Slide 40: Carbon Dioxide
Toxic at fire suppression levels
Storage
  Gas or solid at normal atmospheric pressure
Solid form (dry ice)

## Slide 41: Carbon Dioxide

## Slide 42: Carbon Dioxide
Liquid can exist at elevated pressures.
Triple point
Critical temperature
Vessels can hold 3× as much CO2 as nitrogen.

## Slide 43: Carbon Dioxide
Hand-held extinguishers
High vapor pressure
Cooling effect of CO2

## Slide 44: Perfluorocarbons
Fully fluorinated hydrocarbons
Inert closed spaces against ignition
Smallest molecules stored as compressed gases at high pressures
Larger molecules
Rapid discharge

## Slide 45: Perfluorocarbons
High heat capacities
Concentrations needed for inerting a space
Long atmospheric lifetime
Global warming potential
Use restricted by EPA
Perfluoroethylisopropyl ketone (C6F12O)

## Slide 46: Active Halogenated Agents
Chemical derivatives of simple organic molecules
Liquids stored in pressurized tanks
Exist as gases at atmospheric pressure and normal temperatures
Classified as clean agents

## Slide 47: Active Halogenated Agents
Inclusion of bromine or iodine atom
Chlorine
Fluorine atoms
Iodine compounds

## Slide 48: Active Halogenated Agents
Halon
  Number up to 5 digits
  First digit = number of carbon atoms
  Succeeding digits = numbers of fluorine, chlorine, bromine, and iodine atoms

## Slide 49: Active Halogenated Agents

## Slide 50: Active Halogenated Agents
Nomenclature for halon:
  Classic chlorine- and bromine-containing fire suppressants
Halogenated compounds
  Halon 1301
  Halon 1211
  Halon 2402

## Slide 51: Active Halogenated Agents

## Slide 52: Active Halogenated Agents
Liquids when stored in pressurized tanks
Rapid delivery of compounds
Halon decomposition
Bromine-containing
Little harmful effect of exposure to halon 1301

## Slide 53: Active Halogenated Agents
Speed of chain reactions in flame propagation
Bromine and chlorine atoms:
    R–H + X → HX + R
    Y + HX → HY + X
    Net: R–H + Y → HY + R
  R–H is an organic molecule.
  X is a halogen atom.
  Y is an H atom, O atom, or OH radical.

## Slide 54: Active Halogenated Agents
Earth’s ozone layer
  Phase out of firefighting halons
  Halon 1301 used in some critical applications
  Atmospheric lifetime
  First generation of replacement chemicals
  Organic compounds that lack bromine or chlorine
  Global warming potential
  Absorption of infrared radiation
  Decreased use

## Slide 55: Active Halogenated Agents
Clean chemical compounds
  Inert gases and mixtures of them
  Phasing out hydrochlorofluorocarbons
  Bromotrifluoropropene testing for handheld extinguishers

## Slide 56: Active Halogenated Agents

## Slide 57: Dry Chemical Agents
Dry chemical powder
  Class B and Class C fires
  Widely dispersed or applied in a stream
10 µm to 75 µm in size
Projected by an inert gas

## Slide 58: Dry Chemical Agents
Process when dry chemical powder is applied to fire:
  Finer particles vaporize.
  Flame-propagating species react.
  Particles shield the fuel surface from flame radiation.
  Powder can smother the fire.

## Slide 59: Dry Chemical Agents
Extinguishing efficiency of the powder depends on the particle surface area.
  Least material needed for flame extinguishment

## Slide 60: Dry Chemical Agents

## Slide 61: Dry Chemical Agents
Special situations:
  Rock dust
  Granules of cellular glass
Difficult to compare effectiveness
Modified laboratory flame apparatus
Monoammonium phosphate

## Slide 62: Dry Chemical Agents
Application of dry chemical agents on electrical fires
Ingredients are nontoxic.
Agents for extinguishing metal fires:
  Powders
  Liquid
  Gases

## Slide 63: Dry Chemical Agents
Metal fires are difficult to extinguish.
  Very high temperatures
  Long cooling times
  Halons should not be used.

## Slide 64: Extinguishment of Flowing Gas Flames
Very difficult to extinguish
Best tactic is to turn off gas flow.
Apply a suppressant to the base of the flame.
Interrupt fresh air supply to the fire.

## Slide 65: Extinguishment of Flowing Gas Flames

## Slide 66: Extinguishment of Flowing Gas Flames
Flooding a compartment:
  Slow process
  Difficult to ensure ignition sources are passivated
  Dangerously low levels of oxygen volume fraction
Flame arrestor

## Slide 67: Extinguishment of a Shallow Liquid Fuel Spill Fire
Burn at a high intensity for short time
Automatic sprinkler system:
  Fire point of liquid is close to or above boiling point of water.
  Liquid is water soluble.
  Liquid is denser than water.

## Slide 68: Extinguishment of a Shallow Liquid Fuel Spill Fire
Sprinkler spray may limit fire damage.
Foam formulation or dry powder system may be required.

## Slide 69: Extinguishment of a Deep Tank Liquid Fuel Fire
Can burn for hours or days
Cover the entire flame in one application.
Foams are ideal agents.
Fire of a liquid flowing from opening in a tank or overflowing from top are usually extinguished only by stopping flow.

## Slide 70: Ultrafast Extinguishment of Fires
Fire must be quenched instantly.
Sensitive sensing
Fast-response flame suppression:
  Storage container under high pressure
  Gas generator

## Slide 71: Ultrafast Extinguishment of Fires
Hybrid version

## Slide 72: Summary
Chemicals that are used to extinguish or control fires can be categorized by the types of fires on which they are effective, the chemical phase, the mechanism of action, the mode of application, and the application system.

## Slide 73: Summary
Water is widely used for fire suppression because it is readily available at low cost, is nonflammable, has a high heat of vaporization and gasifies readily, is nontoxic and does not decompose to form toxic products, and causes only limited property damage when used in moderation.

## Slide 74: Summary
Water delivery and suppression effectiveness can be enhanced with chemical additives.

## Slide 75: Summary
Water should not be used on electrical or metal fires and should be used with caution on liquid fuel fires. For these uses, alternative agents, both chemically inert and chemically active, are available.

## Slide 76: Summary
Powdered agents (dry chemicals) are used on Class B and Class C fires.

## Slide 77: Summary
Inert gases prevent or quench flames by increasing the heat capacity of the atmosphere and diluting the oxygen. Chemically active suppressants generally interfere with the chain propagating and chain branching chemistry in flames. The choice and uses of chemically active agents are limited by their effects on the environment.